One-keystroke system installation
and configuration
Don Law
FLUX May 2010
slides are at flux.donlaw.com

---
Introduction(s)

---
Outline
Brief Introduction to Pre eXecution Environment (PXE)
Brief Introduction to Dynamic Host Configuration Protocol
Brief Introduction to Trivial File Transfer Protocol (TFTP)
Brief Introduction to PXELINUX
Brief Introduction to Desktop Management Interface (DMI)
Brief Introduction to Initial Ramdisk (initrd)
RedHat Kickstart

---
Do you have an IP address for me?
F12/bios
PXE
DHCP server
Yes, and a filename: pxelinux.0
TFTP server
Request pxelinux.0 via TFTP
Pxelinux.0 contents

---
Do you have an IP address for me?
F12/bios
PXE
DHCP server
Yes, and a filename: pxelinux.0
TFTP server
Request pxelinux.0 via TFTP
Pxelinux.0 contents
PXELINUX
Request PXELINUX configuration
PXELINUX configuration via TFTP
Request Linux kernel/initrd via TFTP
Linux kernel and initrd contents

---
Do you have an IP address for me?
F12/bios
PXE
DHCP server
Yes, and a filename: pxelinux.0
TFTP server
Request pxelinux.0 via TFTP
Pxelinux.0 contents
PXELINUX
Request PXELINUX configuration
PXELINUX configuration via TFTP
Request Linux kernel/initrd via TFTP
Linux kernel and initrd contents
Linux
kernel and
kickstart
HTTP server
Request kickstart configuration via HTTP
Kick start configuration/installation files

---
You should know ...
Free and Open-Source tools are available to help you automate much of the work in this talk.

---
You should know ...
Free and Open-Source tools are available to help you automate much of the work in this talk.
But if you use it you won't learn as much.
https://fedorahosted.org/cobbler/
http://www.ultimatedeployment.org

---
Brief Introduction to PXE
Preboot Execution – it runs before any loads from disk
De facto standard from Intel – specification is at http://download.intel.com/design/archives/wfm/downloads/pxespec.pdf
The BIOS has to configure a NIC and use it
Can be in the BIOS of the NIC

---
Brief Introduction to PXE
Does three tasks:
  - Configure an IP address
  - Get a filename
  - TFTP that into memory and jump to it
Also provides run-time services to the loaded program

---
 PXE screenshot

---
 PXE screenshot

---
Brief Introduction to DHCP
Dynamic Host Configuration Protocol
Method to introduce a computer and a network
Obtain IP address usable on the network
  - As well as router and DNS configuration
Useful when you have more computers than IP addresses
Each systems gets a “lease” on an IP address

---
Brief Introduction to DHCP
Dynamic Host Configuration Protocol
Method to introduce a computer and a network

---
DHCP: How it works
Use the network to obtain an IP address
  - But you need an IP address to use the network!
  - Solution: Ultimate broadcast address, 255.255.255.255
  - Routers will not pass packets with this target

---
DHCP: How it works
Use the network to obtain an IP address
  - But you need an IP address to use the network!
  - Solution: Ultimate broadcast address, 255.255.255.255
  - Routers will not pass packets with this target
dhcpd listens for broadcasts to 255.255.255.255
Replies with an offer of an IP address lease
  - Along with other network information
RFC 2131 for IPv4, RFC 3315 for IPv6

---
DHCP request on the wire

---
On the wire – request parameters

---
DHCP: Setting up a server
Open source from ISC
  - http://www.isc.org/software/dhcp
Highly likely to be packaged for your distribution
  - yum install dhcp
Edit /etc/dhcpd.conf

---
DHCP: /etc/dhcpd.conf
Parameters can be global, subnet-specific, or host-specific
Specify network to serve
Range of IP addresses to lease out
Default router (option routers)
File to upload (filename)
Server to get file from (next-server)

---
DHCP: /etc/dhcpd.conf
Edit the file (see next slide)
Start the server
See what you did wrong

---
DHCP: Starting the server
# See man dhcpd.conf
subnet 192.168.120.0 netmask 255.255.255.0 {
  range 192.168.120.150 192.168.120.199;
  option routers 192.168.120.120;
  filename "pxelinux.0";
  next-server 192.168.120.120;
}
service dhcpd start
chkconfig --levels 345 dhcpd on

---
DHCP: The offer on the wire

---
Brief Introduction to TFTP
Like FTP for microcontrollers
TFTP
FTP
RFC1350 is 472 lines
Requires UCP
No connection (lock step ack)
No authentication
Simplified directories
RFC is 3120 lines
Requires TCP
Requires multiple connections
Requires authentication

---
Setting up a TFTP server
http://www.kernel.org/pub/software/network/tftp
yum install tftp-server
In /etc/xinet.d/tftp:
  - Change “disable=yes” to “disable=no”
  - Make note of server_args:
    - server_args -s /var/lib/tftpboot
If not already done:
  - service xinetd start
  - chkconfig --levels 345 xinetd on

---
Brief Introduction to PXELINUX
In the same family as SYSLINUX and ISOLINUX
Doesn't contain Linux
Only job is to load and start a Linux kernel
http://syslinux.zytor.com
http://www.kernel.org/pub/linux/utils/boot/syslinux/syslinux-3.86.tar.gz
tar -xzf syslinux-3.86.tar.gz
cp syslinux-3.86/core/pxelinux.0 \
/var/lib/tftpboot

---
Configuration of PXELINUX
Obviously, you can't configure it with config files on the target system.
PXELINUX “phones home” to the IP address it loaded from and looks for a remote config file via TFTP
Searches in pxelinux.cfg directory from most specific to least specific file based on MAC and then IP (in hex).

---
Configuration of PXELINUX
If the MAC address of the interface is 00:90:fb:0d:23:a0, then the first file fetched by TFTP from pxelinux.cfg will be named: 00-90-fb-0d-23-a0
If not found, and if PXELINUX was loaded on an interface with the address of 192.168.120.150, then the following files are attempted until one works:
C0A87896
C0A8789
C0A878
C0A87
C0A8
C0A
C0
C
default

---
Configuration of PXELINUX
The contents of the PXELINUX config file looks a lot like a GRUB config file:
# This is the pxelinux config file
timeout 5
prompt 1
default 1
label 1
        kernel vmlinuz.centos52
        append initrd=initrd.centos52 ╗
ks=http://192.168.120.120/ks/scat-ks.cfg ╗ ip=192.168.120.150 netmask=255.255.255.0

---
Brief Introduction to Desktop Management Interface (DMI)
The OS can discover machine-specific information
A standard has emerged:
  - http://www.dmtf.org/standards/dmi
Linux kernel supports the standard
dmidecode is the user-level interface to the drivers
  - http://www.nongnu.org/dmidecode
Or simply: yum install dmidecode

---
Brief Introduction to initrd
RAM disk that is present as soon as the kernel starts
Commonly used to load storage device drivers
Support must be compiled into the kernel (not a module)

---
Brief Introduction to initrd
RAM disk that is present as soon as the kernel starts
Commonly used to load storage device drivers
Support must be compiled into the kernel (not a module)
We will use it to hold user-level commands and scripts
Commonly found in /boot
A good starter is on the distribution CD in the isolinux directory

---
Brief Introduction to initrd
[root@calli kickstart]# gunzip < initrd-hrvst.gz > initrd-hrvst
[root@calli kickstart]# losetup /dev/loop0 $PWD/initrd-hrvst
[root@calli kickstart]# mkdir hrvst
[root@calli kickstart]# mount /dev/loop0 $PWD/hrvst
[root@calli kickstart]# ls hrvst
bin etc install linuxrc mnt pxebin sys usr
dev initrd lib lost+found proc sbin tmp var
[root@calli kickstart]#
http://www.ibm.com/developerworks/linux/library/l-initrd.html

---
Automated System Inventory

---
Automated system inventory
Script to assemble initrd
Script that is run in initrd
Watch out for module problems

---
Kickstart

---
Kickstart
A replay-able archive of your installation choices
When you install a RedHat-like distribution from CD-ROM, you make a series of choices from menus:
  - Type of keyboard
  - Disk layout
  - Root password
  - Firewall configuration
  - Packages to install
  - etc.

---
Kickstart
All of your choices are stored in:
  - /root/anaconda-ks.cfg
# Kickstart file automatically generated by anaconda.
install
cdrom
lang en_US.UTF-8
keyboard us
xconfig --startxonboot
network --device eth0 --bootproto static --ip 192.168.120.14 --netmask 255.255.255.0 --gateway 192.168.120.111 --nameserver 69.89.79.162,69.89.69.162 --hostname calliope.donlaw.net
firewall --disabled
authconfig --enableshadow --enablemd5
selinux --enforcing
timezone America/New_York
bootloader --location=partition --driveorder=sda,sdb --append="rhgb quiet"

---
Kickstart
When you start a new installation, you can tell the installation process to make all its choices from the kickstart file instead of the menus.
  - You can remake the boot disk to contain your kickstart file.
  - You can tell the install kernel to use a kickstart file on the network.
We're going to load the install kernel over the network, so we will choose the latter.

---
Glue
PXELINUX will load a kernel
  - We give it the install kernel from the CD-ROM
PXELINUX will setup a initrd
  - We give it the initrd that has the install scripts
PXELINUX will pass the URL of the kickstart file to the kernel
  - We will make it available via HTTP
The kickstart file has the URL of the install images
  - We mount the install media where Apache can see it

---
Glue
[root@f12d620 ~]# cd /var/www/html/
[root@f12d620 html]# mkdir centos52
[root@f12d620 html]# mount /dev/cdrom /var/www/html/centos52
mount: block device /dev/sr0 is write-protected, mounting read-only
[root@f12d620 html]# cd centos52/
[root@f12d620 centos52]# ls isolinux/
boot.cat initrd.img memtest rescue.msg vmlinuz
boot.msg isolinux.bin options.msg splash.lss
general.msg isolinux.cfg param.msg TRANS.TBL
[root@f12d620 centos52]# cp isolinux/vmlinuz /var/lib/tftpboot/vmlinuz.centos52
[root@f12d620 centos52]# cp isolinux/initrd.img /var/lib/tftpboot/initrd.centos52
[root@f12d620 centos52]#

---
Demo

---
Questions?